## Slide 1
Analysis and performance evaluation of Kitting Processes
Eline De Cuypere
SMACS research group Department of Telecommunication and Information Processing St.-Pietersnieuwstraat 41, 9000 Gent; Eline.DeCuypere@UGent.be
joint work with Dieter Fiems and Herwig Bruneel
Kitting Process
Model 1
Two equal and indepentent Interrupted Poisson Processes.
Kitting Models
Two equal and indepentent
Poisson Processes.
Numerical Examples
Results
Parameters
Base Model
λ1 = 0.8 μ = 1
λ2= 0.8
Model 1
λ1* = 2 α = 0.25
λ2 = 0.8 β = 0.1667
μ = 1
Model 2
λ1* = [0 2 0 2] A =
λ2* = [0 0 2 2]
μ = [1 1 1 1]
Base Model
Model 2
Arrivals of part 1: Interrupted Poisson Process,
Arrivals of part 2: Poisson Process.
For part 1 in Model 1 and part 1 & 2 in Model 2 we assume a 40% effective production time. The time length is equal to 10.
To ensure a same total 80% production time for all models, the « interrupted » parts arrive at an intensity equal to 2.
Strategy for supplying materials to an assembly line,
The parts necessary for assembly are collected into a container referred to as « kit », prior arriving at an assembly unit,
Kitting Process defined as a Continuous Time Markov Chain.
Methodology
Sparse matrix techniques
  solution for the « steady state explosion »
  iterative solution: the Generalized Minimal Residual Method.
The larger the capacity, the smaller the probability that the buffer is full,
Interruptions in the production of one part have a greater impact on the buffer of the other part than on its own,
Adding a production interrupted component to part 2 doesn’t have a significant impact on the probability.
Buffer 1
Buffer 2
Future research
Expansion of the models to more than 2 parts,
Calculation of other performance measures such as kit earliness or inertia,
Integration of kitting in a production process,
Cost calculation of the process,
Application of the technique in other domains such as telecommunication systems.
Notes: <number>