## Slide 1
Analysis and performance evaluation of Kitting Processes
Eline De Cuypere
SMACS research group Department of Telecommunication and Information Processing St.-Pietersnieuwstraat 41, 9000 Gent; Eline.DeCuypere@UGent.be
joint work with Dieter Fiems
Kitting Process
Model 2:
« Production interruptions »
at part 1
Two equal and indepentent Interrupted Poisson Processes.
Kitting Models
Two equal and indepentent
Poisson Processes.
Numerical Examples:
Probability that buffer 1 and 2 are full
Model 1:
« Efficient production »
Model 3:
« Production interruptions »
at both parts
Arrivals of part 1: Interrupted Poisson Process,
Arrivals of part 2: Poisson Process.
Strategy for supplying materials to an assembly line.
The parts necessary for assembly are collected into a container
or kit, prior to arriving at an assembly unit.
Future research
Expansion of the models to more than 2 parts.
Calculation of other performance measures such as kit earliness or tardiness.
Integration of kitting in a production process.
Cost calculation of the process.
Three Markovian queues models for kitting processes
with two parts.
Methodology
Sparse matrix technique
Solution for the « state space explosion problem » due to multidimensionality of the state space (2 buffers).
  Sparse generator matrix
  Use of the GMRES Method (General Minimal Residual
  Method) to solve the balance equations.
The larger the capacity, the smaller the probability that the buffer is full.
Interruptions in the production of part 1 have a greater impact on the
buffer 2 than on its own buffer (buffer 1).
Adding production interruptions for part 2 doesn’t have a significant
impact on the probability for buffer 2 but does for buffer 1.
Results
Buffer 1
Parameters
All models  80 % load.
Production interruptions  on average 10 kits can be
produced during a production period of 10.
The production is interrupted 40 % of the time.
Buffer 2
Notes: <number>