## Slide 1: CS 5253 Workshop 1
MAC Protocol and Traffic Model

## Slide 2: Objectives
Get familiar with OPNET, a tool for network simulation.
Use OPNET to study CSMA/CD channel access and traffic modeling.
References:
Joseph L. Hammond, and Petter J. P. O’Reilly, Performance Analysis of Local Computer Networks, Addison_Wesley Publishing Company,1986.
Gary N. Higginbottom, Performance Evaluation of Communication Networks, Artech House, 1998

## Slide 3: Medium Access Control
Medium Access Control (MAC):
  How to share a common medium among the users?
MAC layer is very important in LANs, nearly all of which use a multiaccess channel as the basis of their communication.

## Slide 4: ALOHA Protocol
ALOHA is developed in the 1970s at the University of Hawaii.
The basic idea is simple:
  Let users transmit whenever they have data to be sent.
If two or more users send their packets at the same time, a collision occurs and the packets are destroyed.

## Slide 5: ALOHA Protocol
If there is a collision,
  the sender waits a random amount of time and sends it again.
The waiting time must be random. Otherwise, the same packets will collide again.

## Slide 6: A Sketch of Frame Generation
Note that all packets have the same length because the throughput of ALOHA systems is maximized by having a uniform packet size.

## Slide 7: Throughput
Throughput:
  The number of packets successfully transmitted through the channel per packet time.
What is the throughput of an ALOHA channel?

## Slide 8: Assumptions
Infinite population of users
New frames are generated according to a Poisson distribution with mean S packets per packet time.
  Probability that k packets are generated during a given packet time:

## Slide 9: Observation on S
If S > 1, packets are generated at a higher rate than the channel can handle.
Therefore, we expect
0 < S < 1
If the channel can handle all the packets, then S is the throughput.

## Slide 10: Packet Retransmission
In addition to the new packets, the stations also generate retransmissions of packets that previously suffered collisions.
Assume that the packet (new + retransmitted) generated is also Poisson with mean G per packet time.

## Slide 11: Relation between G and S
Clearly,
At low load, few collisions:
At high load, many collisions:
Under all loads,
where P0 is the probability that a packet does not suffer a collision.

## Slide 12: Vulnerable Period
Under what conditions will the shaded packet arrive undamaged?

## Slide 13: Throughput
Vulnerable period: from t0 to t0+2t
Probability of no other packet generated during the vulnerable period is:
Using S = GP0, we get

## Slide 14: Relation between G and S
Max throughput occurs at G=0.5, with S=1/(2e)=0.184.
Hence, max. channel utilization is 18.4%.

## Slide 15: Slotted ALOHA
Divide time up into discrete intervals, each corresponding to one packet.
The vulnerable period is now reduced in half.
Probability of no other packet generated during the vulnerable period is:
Hence,

## Slide 16: Carrier Sense
In many situations, stations can tell if the channel is in use before trying to use it.
If the channel is sensed as busy, no station will attempt to use it until it goes idle.
This is the basic idea of the Carrier Sense Multiple Access (CSMA) protocol.

## Slide 17: CSMA Protocols
There are different variations of the CSMA protocols:
  1-persistent CSMA
  Nonpersistent CSMA
  p-persistent CSMA
We discuss only 1-persistent CSMA.

## Slide 18: 1-persistent CSMA
The protocol:
  Listens before transmits
  If channel busy, waits until channel idle
  If channel idle, transmits
  If collision occurs, waits a random amount of time and starts all over again
It is called 1-persistent because the station transmits with a probability of 1 whenever it finds the channel idle.

## Slide 19: A Comparison

## Slide 20: CSMA/CD Protocol
If two stations transmits simultaneously, they will both detect the collision almost immediately.
Rather than finish transmitting their packets, the stations should stop transmitting as soon as the collision is detected.
This protocol is called CSMA with collision detection (CSMA/CD).

## Slide 21: Traffic Model
Constant-Bit-Rate Traffic
  e.g. traditional (circuit-switched) voice
On-Off Source
  e.g. packetized voice
Poisson Process
  e.g. traditional data traffic
Interrupted Poisson Process (IPP)
  e.g. bursty data traffic
Markov Modulated Poisson Process (MMPP)
  e.g. multimedia traffic

## Slide 22: Constant-Bit-Rate Traffic
Packets are generated at a constant bit rate R.
Packets

## Slide 23: On-Off Source
ON
OFF
Constant bit rate R
Stay in ON state for a period exponentially distributed with mean 1/
Stay in OFF state for a period exponentially distributed with mean 1/

## Slide 24: On-Off Source
exponential with mean 1/
exponential with mean 1/
ON
OFF
ON

## Slide 25: On-Off Source
Let Rm be the mean bit rate. Then
An on-off source is usually specified by the 3 parameters: R, Rm and 1/ (mean burst length).

## Slide 26: Poisson Process
Poisson process with rate 
  Interarrival time is exponentially distributed mean 1/.
interarrival time

## Slide 27: Interrupted Poisson Process (IPP)
ON
OFF
Poisson process with rate 
Stay in ON state for a period exponentially distributed with mean 1/
Stay in OFF state for a period exponentially distributed with mean 1/

## Slide 28: Markov Modulated Poisson Process (MMPP)
Example: 3-state MMPP
Poisson process with rate 1
1
2
3
Poisson process with rate 2
Poisson process with rate 3
p12
p21
p13
p31
p23
p32
Stay in state i for a period exponentially distributed with mean 1/i

## Slide 29: Guideline for Using opnet
You should read the material “Introduction of opnet”, and “Small internet work” before start Aloha tutorial.
Exercise 1: (Individual work, 5% percent for semester B) After trying “Small internet work” , do a further study on the following case:
The company has 3rd floor which contains another 15 computers of the same type connected with a star. Just hand in a hard copy of the figures about the delay and load.(Due week3/week4 on Monday.)