## Slide 1: An Overview of State-of-the-art Denoising and Demosaicking Techniques: Toward A Unified Framework for Handling Artifacts during Image Reconstruction
Bart Goossens, Hiep Luong, Jan Aelterman, Aleksandra Pizurica and Wilfried Philips
Ghent University, TELIN-IPI-iMinds
June 11, 2015
Notes: Abstract:

## Slide 2: Overview
Introduction
Image denoising
Image demosaicking
A unified reconstruction framework
Results
Conclusion

## Slide 3: Overview
Introduction
Image denoising
Image demosaicking
A unified reconstruction framework
Results
Conclusion

## Slide 4
=
Digital photography: more MP
More noise: area of a sensor element (pixel) becomes smaller
Demosaicking: interpolation of missing color pixel intensities
→ noise becomes correlated
Blur (optics, motion) becomes more apparent.
Introduction
Notes: Tendency to push the physical limits of acquisition

## Slide 5
Introduction
Goal: “solve” artifacts (noise, blur) using digital image processing techniques.
Criteria (see also [Hirakawa, 2008]):
Complexity of the implementation
vs
Geforce GTX 980
Geforce GTX 980
Quality of the reconstruction
vs
Quantum efficiency/noise
vs
Robustness to color prior assumptions
vs
Notes: Quantum efficiency: measurement of a device’s electrical sensitivity to light

## Slide 6
Introduction
On-line: within the camera
Off-line: desktop PC software (RawTherapee, Adobe Lightroom)

## Slide 7
RAW image
Image processing chain (simplified):
RAW
Exposure correction
Chromatic
aberration correction
Denoising
demosaicking
Color
correction
Gamma
correction
Deblurring
Output image
HDR synthesis (optional effect)
demosaicking
Color correction
Gamma correction
Deblurring
Output image
Introduction
Notes: Add example images?
Split the slide in two?

## Slide 8
Image processing chain (simplified):
Problems:
Sequential processing (denoising, deblurring and demosaicking) leads to poor image quality due to incorrect interpolation of color intensities and noise.
Pushing acquisition limits (e.g. resolution, noise) => effect becomes more pronounced
Research:
Joint denoising and demosaicking [Hirakawa, 2006], [Condat, 2010], [Chatterjee, 2011]
Joint demosaicking and deconvolution [Paliy, 2008], [Soulez, 2009]
High dynamic range synthesis and denoising [Goossens, 2011b]
Declipping (de-saturation) and denoising [Foi, 2008]
RAW
Exposure correction
Chromatic
aberration correction
Denoising
demosaicking
Color
correction
Gamma
correction
Deblurring
Output image
HDR synthesis (optional effect)
Introduction
Notes: Add example images?
Split the slide in two?

## Slide 9: Overview
Introduction
Image denoising
Image demosaicking
A unified reconstruction framework
Results
Conclusion

## Slide 10
Image denoising techniques
Main principle:
Images consist of smooth areas with discontinuities near edges, textures
Pre-knowledge for image reconstruction method, exploited by
  Either a cost criterion (penalty)
  Or a statistical model
Smooth area
Edge
Texture
Notes: Dandelion

## Slide 11
Image denoising techniques – wavelets, shearlets
Scale 3
Scale 2
Scale 1
Scaling function
Scale 1
Scale 2
Scale 3
Write images as sum of different wavelets/shearlets (with coefficients)
Transform domain: denoising & demosaicking becomes easier!!!
Complex wavelets [Selesnick, 2005]
Shearlets [Kutyniok, 2007], [Goossens, 2011a]

## Slide 12
Waveletcoefficients
0
Peaks correspond to edges
Image denoising techniques

## Slide 13
Image denoising techniques
Example: wavelet-domain soft-thresholding
Wavelet coefficients
0
T
-T
0
After “hard thresholding”

## Slide 14
Image denoising techniques: wavelet-domain techniques
Original
Original+Gaussian Noise (s=50)
Shearlet thresholding
[Goossens, 2011a]+[Chang, 2000]
BLS-GSM + shearlets
[Goossens, 2011a]+[Portilla, 2003]
CPU: 2.6 s | GPU: 0.701 s
CPU: 2.8 s | GPU: 0.733 s
Notes: Lizard
Image size: 400x300, RGB
Shearlet thresholding: 10 s (CPU), 700 ms (GPU)
BLS-GSM: 733 msec (GPU), 2.8 sec (CPU)

## Slide 15
Image denoising techniques: image domain techniques
Original
Original+Gaussian Noise (s=50)
Bilateral filter
[Tomasi, 1998]
Anisotropic diffusion
[Weickert, 1998]
CPU: 0.093 s | GPU: 0.007 s
CPU: 2.180 s | GPU: 0.080 s
Notes: Bilateral filter: 7 ms (GPU), 93 ms (CPU) – 10 iterations
Anisotropic diffusion: 80 ms (GPU), ms (CPU) – 150 iterations (NOTE: calculation time depends on the parameters – step size, number of iterations)

## Slide 16
Image denoising techniques: image domain techniques
Original
Original+Gaussian Noise (s=50)
Non-local means
[Goossens, 2008]
BM3D
[Dabov, 2007]
CPU: 3.3 s | GPU: 0.398 s
CPU: 49 s | GPU: N/A
Notes: Non-local means: (CPU) 3.343 s (GPU) 398 ms
BM3D: (CPU) 49 s

## Slide 17: Overview
Introduction
Image denoising
Image demosaicking
A unified reconstruction framework
Results
Conclusion

## Slide 18
Grid mosaic:
Alternative interpretation:
=
+
+
=
g
+
+
βs
αs
(
(
)
)
-
-
~fully sampled luminance
~subsampled chrominances
Image demosaicking: principle
Main principle: unmixing of the measured color channels!

## Slide 19
π
0
3π/4
Assumption 1:
luminance bandlimited
Assumption 2:
chrominance bandlimited
π
0
π/4
Frequency spectrum
Frequency spectrum
Main principle: unmixing of the measured color channels!
Image demosaicking: principle

## Slide 20
π
0
Bandlimitedness assumptions: exact recovery possible!!!
Main principle: unmixing of the measured color channels!
Image demosaicking: principle

## Slide 21
Image demosaicking: artifacts
Sudden color transition: difficult for demosaicking!

## Slide 22
Blur
Ground truth
Discolorations
Zipper
Image demosaicking: artifacts

## Slide 23
Reference image
Image demosaicking: results
CFA image
DLMMSE
[Zhang, 2005]
Complex wavelet
[Goossens, 2013]
Difference
DLMMSE - ref
Difference
Complex wavelet - ref
DLMMSE
[Zhang, 2005]
Complex wavelet
[Goossens, 2013]

## Slide 24
  Denoising-after-demosaicking: noise is highly correlated due to the interpolation
  Demosaicking-after-denoising: denoising may destroy high-frequency components necessary for demosaicking
  Better: joint denoising and demosaicking: take uncertainty in the edge direction estimation into account
Demos.
Denoise
Denoise
Demos.
Denoise
Demos.
Image denoising+demosaicking

## Slide 25
Unified reconstruction framework
More sophisticated processing (higher complexity?)
Optimally solving the noise and demosaicking problems
Other sensor/lens deficiencies (chromatic aberration, cross-talk, fixed pattern noise, …)
A unified reconstruction framework: overview
Notes: TODO: add pictures

## Slide 26
A unified reconstruction framework: overview
RAW
input image
Degradation model
(blur, signal-dependent noise,
demosaicking…)
Iterative
solver
Updated
RAW image
Impose prior knowledge
w.r.t. undegraded image
(e.g., wavelets, shearlets)
Reconstructed
image
RAW
Exposure correction
Chromatic
aberration correction
Denoising
demosaicking
Color
correction
Gamma
correction
Deblurring
Output image
In the loop

## Slide 27
…
t0 t1 t2 … t31
…
…
t0 t1 t2 … t31
…
Block 1 Warps
Block 2 Warps
SP
SP
SP
SP
SFU
SP
SP
SP
SP
SFU
Instruction Fetch/Dispatch
Instruction L1
Streaming Multiprocessor
Shared Memory
…
t0 t1 t2 … t31
…
Block 1 Warps
Core 1
Core 2
Core 3
Core 4
GPU
CPU
Nvidia CUDA
OpenCL
GCC
Quasar
OpenGL / DirectX
Real-time
visualization
FFMPEG / DirectShow
Video input
Quasar: new programming language for CPU and GPU
http://quasar.ugent.be [Goossens, 2014]

## Slide 28
Quasar: new programming language for CPU and GPU
Easy development and debugging of image reconstruction algorithms!
http://quasar.ugent.be [Goossens, 2014]

## Slide 29
Results
RawTherapee (default profile)
Our unified reconstruction framework

## Slide 30: Conclusion
Pushing physical limits of sensors
› need for better reconstruction techniques
Image denoising & demosaicking
Other post-processing steps (gamma correction, chromatic aberration correction, etc.) to be considered
Sequential approach: not optimal!
Unified reconstruction framework
New programming language Quasar helps to develop and debug new reconstruction algorithms

## Slide 31: Questions?

## Slide 32: Bibliography (I)
[Buades, 2005] A. Buades., B. Coll., and J. Morel, “A non local algorithm for image denoising,” SIAM interdisciplinary journal: Multiscale Modeling and Simulation, vol. 2, no. 2, pp. 60–65, 2005.
[Chang, 2000] Chang, S., Yu, B., and Vetterli, M. Spatially adaptive wavelet thresholding with context modeling for image denoising. IEEE Trans. Image Process., 9(9):1522–1531, 2000.
[Chatterjee, 2011] P. Chatterjee, N. Joshi, K. S. B., and Y. Matsushita, “Noise suppression in low-light images through joint denoising and demosaicing,” in Proc. IEEE Conf. Computer Vision and Pattern Recognition (CVPR), 2011, pp. 321–328.
[Condat, 2010] L. Condat, “A simple, fast and efficient approach to denoisaicking: Joint demosaicking and denoising,” in Proc. 17th IEEE Int Conf. Image Processing (ICIP), Hong Kong, China, 2010, pp. 905–908.
[Dabov, 2007] K. Dabov, A. Foi, V. Katkovnik, and K. Egiazarian, “Image denoising by sparse 3d transform-domain collaborative filtering,” IEEE Transactions on image processing, vol. 16, no. 8, pp. 2080–2095, 2007.
[Foi, 2008] A. Foi, “Practical denoising of clipped or overexposed noisy images,” in Proc. 16th European Signal Process. Conf. (EUSIPCO), Lausanne, Switzerland, 2008

## Slide 33: Bibliography (II)
[Goossens, 2008] B. Goossens, H. Luong, A. Pižurica, and W. Philips, “An improved Non-Local Means Algorithm for Image Denoising,” in 2008 International Workshop on Local and Non-Local Approximation in Image Processing, Ghent, Belgium, dec 2008
[Goossens, 2011a] B. Goossens, J. Aelterman, H. Luong, A. Pizurica and W. Philips, "Design of a Tight Frame of 2D Shearlets Based on a Fast Non-iterative Analysis and Synthesis Algorithm, " SPIE Optics & Photonics 2011, Wavelets and Sparsity XIV, Aug. 21-25, San Diego, CA, USA, p. 81381Q (13 pages)
[Goossens, 2011b] B. Goossens, H. Luong, J. Aelterman, A. Pižurica, and W. Philips, “Reconstruction of High Dynamic Range Images with Poisson Noise Modeling and Integrated Denoising,” in IEEE Int. Conf. Image Processing (ICIP2011), Brussels, Belgium, Sept. 11-14 2011, pp. 3429–3432
[Goossens, 2013] B. Goossens, J. Aelterman, H. Luong, A. Pižurica, and W. Philips, “Complex wavelet joint denoising and demosaicing using gaussian scale mixtures,” in IEEE Int. Conf. Image Processing, Melbourne, Australia, Sept. 15-18 2013, pp. 445–448
[Goossens, 2014] B. Goossens, J. De Vylder and W. Philips, "Quasar - a New Heterogeneous Programming Framework for Image and Video Processing Algorithms on CPU and GPU, " IEEE Int. Conf. on Image Processing (ICIP2014), Oct. 27-30, 2014, Paris, France, p. 2183-2185.

## Slide 34: Bibliography (III)
[Gunturn, 2005] B. Gunturk, J. Glotzbach, Y. Altunbasak, R. Schaffer, and R. Mersereau, “Demosaicing: color filter array interpolation,” IEEE Sig. Proc. Magazine, vol. 22, no. 1, pp. 44–54, 2005.
[Hirakawa, 2006] K. Hirakawa and T. W. Parks, “Joint demosaicing and denoising,” IEEE Trans. Image Process., vol. 15, no. 8, pp. 2146–2157, aug 2006.
[Hirakawa, 2008] Hirakawa, K. and Wolfe, P. J., Spatio-spectral color filter array design for optimal image recovery. IEEE Trans. Image Processing, 17(10):1876–1890, 2008.
[Kutyniok, 2007] G. Kutyniok and D. Labate, “Construction of Regular and Irregular Shearlets,” J. Wavelet Theory and Appl., vol. 1, pp. 1–10, 2007
[Luong, 2012] H. Luong, B. Goossens, J. Aelterman, A. Pižurica, and W. Philips, “A Primal-Dual Algorithm for Joint Demoisaicing and Deconvolution,” in IEEE Int. Conf. Image Processing (ICIP2012), Orlando, Florida, USA, Sep. 30 - Oct. 3 2012, pp. 2801–2804.
[Paliy, 2008] D. Paliy, A. Foi, R. Bilcu, V. Katkovnik, and K. Egiazarian, “Joint deblurring and demosaicking of Poissonian Bayer-data based on local adaptivity,” in Proc. European Sig. Proc. conf. (EUSIPCO), 2008
[Portilla, 2003] J. Portilla, V. Strela, M. Wainwright, and E. Simoncelli, “Image denoising using scale mixtures of gaussians in the wavelet domain,” IEEE Trans. on image processing, vol. 12, no. 11, pp. 1338–1351, Nov. 2003.

## Slide 35: Bibliography (IV)
[Selesnick, 2005] I. W. Selesnick, R. G. Baraniuk, and N. G. Kingsbury, “The Dual-Tree Complex Wavelet Transform,” IEEE Signal Processing Magazine, vol. 22, no. 6, pp. 123–151, nov 2005.
[Soulez, 2009] F. Soulez and E. Thiebaut, “Joint deconvolution and demosaicking,” in Proc. IEEE Int. Conf. Image Proc., 2009, pp. 145–148.
[Tomasi, 1998] C. Tomasi and R. Manduchi, “Bilateral filtering for gray and color images,” International Conference on Computer Vision (ICCV), pp. 839–846, 1998.
[Weickert, 1998] J. Weickert, Anisotropic Diffusion in Image Processing, ser. ECMI Series. Teubner-Verlag, 1998.
[Zhang, 2005] Zhang, L. and Wu, X. Color demosaicking via directional linear minimum mean square-error estimation. IEEE Transactions on Image Processing, 14(12):2167–2178, 2005.